Supplementary information for:

Dynamics of microbial community functional structure visualized by GeoChip during the in-situ bioremediation of a uranium-contaminated aquifer

Joy D. Van Nostrand1,2,†, Liyou Wu1,†,Wei-Min Wu3, Zhijian Huang5, Terry J. Gentry4, Ye Deng1, Jack Carley6, Sue Carroll6, Zhili He1,2, Baohua Gu6, Jian Luo7, Craig S. Criddle3, David B. Watson6, Philip M. Jardine6, Terence L. Marsh8, James M. Tiedje8, Terry C. Hazen2,9, Jizhong Zhou1,2,9

†These authors contributed equally to this work

1Institute for Environmental Genomics and Department of Botany and Microbiology, University of Oklahoma, Norman, OK, USA; 2Virtual Institute for Microbial Stress and Survival, http://vimss.lbl.gov; 3Department of Civil and Environmental Engineering, Stanford University, Stanford, CA, USA; 4Department of Soil and Crop Sciences, Texas A&M University, College Station, TX, USA; 5State Key Laboratory of Biocontrol, School of Marine Sciences, School of Life Sciences, Sun Yat-sen University, Guangzhou, PR China; 6Environmental Sciences Division, Oak Ridge National Laboratory, Oak Ridge, TN, USA; 7Department of Civil & Environmental Engineering, Georgia Institute of Technology, Atlanta, GA, USA; 8Center for Microbial Ecology, Michigan State University, East Lansing, MI, USA and 9Earth Sciences Division, Lawrence Berkeley National Laboratory, Berkeley, CA, USA

| TABLE S2. Percentage of unique (bolded) and overlapped (italicized) genes detected and diversity indices from each time point in Well FW101-2 |
| --- |
| Sample name | Day166 | Day248 | Day255 | Day298 | Day622 | Day641 | Day670 | Day719 |
| Day166 | 6.28 | 62.32 | 26.99 | 49.06 | 41.94 | 18.87 | 6.72 | 30.74 |
| Day248 |  | 9.32 | 27.04 | 48.08 | 39.91 | 18.71 | 7.13 | 30.98 |
| Day255 |  |  | 29.58 | 22.93 | 24.95 | 30.37 | 13.34 | 29.66 |
| Day298 |  |  |  | 6.81 | 45.19 | 15.74 | 6.5 | 31.95 |
| Day622 |  |  |  |  | 1.43 | 24.88 | 9.03 | 37.22 |
| Day641 |  |  |  |  |  | 13.04 | 16.95 | 31.02 |
| Day670 |  |  |  |  |  |  | 20 | 11.89 |
| Day719 |  |  |  |  |  |  |  | 3.87 |
| Total no. of genes detected | 1211 | 1352 | 1650 | 998 | 769 | 767 | 330 | 724 |
| Shannon | 6.905 | 7.002 | 7.226 | 6.659 | 6.514 | 6.43 | 5.625 | 6.384 |
| Simpson | 823.68 | 896.69 | 1139.93 | 615.65 | 593.01 | 494.34 | 231.22 | 482.44 |
| SimpsonE | 0.68 | 0.663 | 0.691 | 0.617 | 0.771 | 0.645 | 0.701 | 0.666 |

TABLE S1 is available as an Excel Sheet at the Applied and Environmental Microbiology website.

| TABLE S3. Percentage of unique (bolded) and overlapped (italicized) genes detected and diversity indices from each time point in FW102-3 (%) |
| --- |
| Sample name | Day166 | Day191 | Day212 | Day226 | Day233 | Day248 | Day255 | Day304 | Day622 | Day641 | Day670 | Day705 | Day719 |
| Day166 | 3.59 | 27.97 | 28.47 | 26.28 | 33.7 | 26.34 | 30.53 | 23.3 | 13.53 | 21.83 | 27.15 | 23.07 | 20.39 |
| Day191 |  | 2.67 | 58.93 | 57.48 | 51.54 | 59.98 | 61.75 | 49 | 9.95 | 18.98 | 22.2 | 21.99 | 16.05 |
| Day212 |  |  | 6.44 | 61.31 | 53.48 | 50.4 | 53.32 | 38.47 | 8.7 | 21.78 | 29.69 | 29.19 | 16.16 |
| Day226 |  |  |  | 7.25 | 48.25 | 50.96 | 50.8 | 38.46 | 7.85 | 21.69 | 26.34 | 29.5 | 15.27 |
| Day233 |  |  |  |  | 0.97 | 46.68 | 54.02 | 40.24 | 12.65 | 24.11 | 28.48 | 26.26 | 20.56 |
| Day248 |  |  |  |  |  | 1.31 | 60.79 | 50.97 | 10.98 | 18.98 | 19.42 | 19.27 | 17.48 |
| Day255 |  |  |  |  |  |  | 0.68 | 56.59 | 11.35 | 18.25 | 21.41 | 18.89 | 16.33 |
| Day304 |  |  |  |  |  |  |  | 1.93 | 7.3 | 9.77 | 14.18 | 10.85 | 6.86 |
| Day622 |  |  |  |  |  |  |  |  | 3.76 | 24.85 | 15.63 | 11.58 | 20.73 |
| Day641 |  |  |  |  |  |  |  |  |  | 5.42 | 31.41 | 33.58 | 27.73 |
| Day670 |  |  |  |  |  |  |  |  |  |  | 8.29 | 42.37 | 18.34 |
| Day705 |  |  |  |  |  |  |  |  |  |  |  | 18.52 | 19.22 |
| Day719 |  |  |  |  |  |  |  |  |  |  |  |  | 9.78 |
| Total No. of genes detected | 808 | 1425 | 1895 | 1849 | 1239 | 1149 | 1176 | 880 | 266 | 794 | 1206 | 1593 | 491 |
| Shannon | 6.39 | 7.04 | 7.32 | 7.31 | 6.87 | 6.9 | 6.89 | 6.55 | 5.38 | 6.53 | 6.9 | 7.22 | 5.95 |
| Simpson | 402.5 | 922 | 1213.4 | 1226.1 | 746.3 | 859.1 | 823.4 | 569.4 | 171.2 | 583.8 | 801.2 | 1167.5 | 291.6 |
| Simpson E | 0.498 | 0.647 | 0.64 | 0.663 | 0.602 | 0.748 | 0.7 | 0.647 | 0.644 | 0.735 | 0.664 | 0.733 | 0.594 |

FIG. S1.  Map of the bioremediation test site.  Surface view of wells (A), squares indicate injection (FW024 and FW104) and extraction wells (FW026 and FW103), circles with an x indicate monitoring wells (FW100, FW101, and FW102).  Belowground view (B), thick blue arrow indicates where clean water was injected, thin blue arrows indicate water circulation, thick red arrow indicates where the electron donor was injected, thin red arrows indicate circulation.  The center well indicated the location of the three monitoring wells with sampling depth indicated by the numbers 1-4.

A flow-field created by injection of clean water to the outer loop protects the inner loop from invasion of contaminated groundwater.  Intermittent ethanol injections [120-150 mg L-1 chemical oxygen demand (COD)] into the inner loop (FW104) occurred from days 137-535 as electron donors for U(VI) reduction.  DO in the aquifer is naturally low (0-0.3 mg L-1); but, during the initial 638 days of operation, DO penetrated the treatment area via injection of clean water.  After day 638, Na2SO3 was added to reduce DO.

FIG. S2.  Detrended correspondence analysis of functional genes and geochemistry.  Functional genes detected using GeoChip 2.0 (A) and all geochemistry values (B) were used for DCAs.  The numbers next to each symbol indicate the operational day corresponding to sample collection.  The colors represent the monitoring well sampled and are indicated by the key in (B).

FIG. S3.  Hierarchical cluster analysis of all genes detected in all MLS wells.  Results were generated in CLUSTER and visualized in TREEVIEW.  Red indicates signal intensities above background and black indicates signals below background.  Higher intensity reds indicate higher signal intensities.  Graphs to right indicate average signal intensities of each group.  Groups were determined based on clustering of genes and are indicated by numbers on the left side of the tree.

FIG. S4.  Relative abundance of functional gene categories within each division.  Divisions are based on the functional gene tree in Figure S2.

FIG. S6.  Relative abundance of all functional gene groups detected.  The total number of genes detected at each time point was used to calculate the relative abundance of each gene group from FW101-2 and FW102-3.  Numbers along x-axis are operational day.

FIG. S7.  Abundance of metal reducing populations.  Relative abundance of dsr, nitrate/nitrite reduction, and cytochrome c genes was determined using total signal intensity of each gene group.  FW101-2, A; FW103-2, B.

FIG. S8.  Hierarchical cluster analysis of functional genes in FW101-2.  Cluster analysis was done for cytochrome c (A), dsr (B), and nitrate/nitrite reduction (C) genes.  Results were generated in CLUSTER and visualized using TREEVIEW.  Red indicates signal intensities above background while black indicates signal intensities below background.  Brighter red coloring indicates higher signal intensities.

FIG. S9.  Hierarchical cluster analysis of functional genes in FW102-3.  Cluster analysis was done for cytochrome c (A), dsr (B), and nitrate/nitrite reduction (C) genes.  Results were generated in CLUSTER and visualized using TREEVIEW.  Red indicates signal intensities above background while black indicates signal intensities below background.  Brighter red coloring indicates higher signal intensities.

# Text boxes

FIG. S5.  Detrended correspondence analysis of functional gene groups.  The functional genes dsr (A), cytochrome c (B), and denitrification genes (C) detected using GeoChip 2.0 were used for analysis.  The numbers next to each symbol indicate the operational day corresponding to sample collection.  The colors represent the monitoring well sampled and are indicated by the key in (C).

D269

0

FW102

-

3

D298

D323

FW102

-

2

D278

D248

D255

D304

FW101

-

2

D622

D642

D719

D248

D298

0

40

80

10

D248

D184

D670

d212

D226

D233

D255

D622

D705

D255

D622

D719

D670

D163

D166

D166

D191

D642

D670

D719

D166

D642

20

(B) Geochemistry

(A) Functional genes

20%

0%

40%

60%

80%

100%

166

248

255

298

622

641

670

719

Relative Abundance

Sampling Day

FW101-2

A.

(C) Denitrifying genes

B.

Metal resistantance

Cytochrome C

dsrAB

Denitrification

Organic degradation

Nitrification

Nitogen fixation

Methane oxidation

Methane generation

Carbon Fixation

Carbon degradation

B.

A.